## Slide 1: Patient Specific 3D Surfaces for Interactive Medical Planning and Training
Felix G. Hamza-Lup, Ph.D.
Associate Professor Computer Science
and Information Technology
Armstrong State University
Savannah GA, USA
20th International Conference on 3D Web Technology (Web3D 2015), June 18-21, Heraklion, Crete, Greece

## Slide 2: Outline
Background and Motivation
Related work;
  Surface Scanning – Technology
  3DRTT
Proposed Scanning System
  Configuration Scenarios
  Accuracy Assessment
Data Processing and Optimization
20th International Conference on 3D Web Technology (Web3D 2015), June 18-21, Heraklion, Crete, Greece

## Slide 3: Background (1)
Radiotherapy is a complex procedure for cancer treatment commonly administered in conjunction with other forms of cancer management like surgery and chemotherapy.
50-60% of cancer patients are treated with radiation at different stages (www.radiologyinfo.org)
20th International Conference on 3D Web Technology (Web3D 2015), June 18-21, Heraklion, Crete, Greece

## Slide 4: Background (2)
External beam radiotherapy systems:
  X-Ray Therapy (XRT)
  Proton Therapy (PT)
20th International Conference on 3D Web Technology (Web3D 2015), June 18-21, Heraklion, Crete, Greece

## Slide 5: Motivation (1)
Accurately predicting and preventing collisions among different hardware system components and the patient to avoid re-planning

## Slide 6: Motivation (2)
Simulation tool for realistic representation of the treatment room with as much detail and resolution as possible
Interactivity for configuration and visualization of different systems components (table, collimator, devices, beams etc…)
Simple, web-enabled interface to facilitate collaboration and reduce overhead and cognitive load
Uses:
  Clinical – planning phase
  Teaching
  Patient education
20th International Conference on 3D Web Technology (Web3D 2015), June 18-21, Heraklion, Crete, Greece

## Slide 7: Related Work – 3DRTT
X-Ray Therapy Simulator (2007-2014)
  Accurate hardware models but
  Generic patient model
http://3drtt.org/

## Slide 8: Related Work – 3D scanning
We want:
  Real-time 3D patient models
      &
  Inexpensive/reconfigurable solution
Hardware and Software …
Name | Operating range | Frame Speed | Accuracy | Scanner Type
Kinect ($250) | [0.4 ,4] m* | 30Hz | 3mm @ 1.0m# | NCA Structured Light
Kinect v2 ($200) | [0.5, 4.5] m* | 30Hz | 1mm @ 1m# | NCA Time of Flight
Sense ($500) | [0.4 ,3.5] m* | 30Hz | 1mm @ 0.5m$ | NCA Structured Light
SCANIFY ($1500) | [0.35, 0.45] m | 10Hz | 350 microns$ | NCP Stereoscopic and photometric
David SLS-2 ($3000) | [0.4, ∞) m | 30Hz | <1% of length$ | NCA Structured Light
* Accuracy is reduced with distance. $ Advertised accuracy # Reduced field-of-view. See section 3.3. |  |  |  | 
20th International Conference on 3D Web Technology (Web3D 2015), June 18-21, Heraklion, Crete, Greece

## Slide 9: Proposed Scanning System
Accuracy of MK vs MKv2:

## Slide 10: Proposed Scanning System
Based on Microsoft Kinect (v2)
Configuration scenarios:

## Slide 11: IR Camera Calibration
Calibration procedure (Kahlesz et al. [2007]. )
In practice must be done one time – since the treatment system is based on optical precision tables.
20th International Conference on 3D Web Technology (Web3D 2015), June 18-21, Heraklion, Crete, Greece

## Slide 12: Data Processing and Optimization (1)
Polygonal Mesh Optimization
  Point clouds are processed using the Poisson Surface Reconstruction (PSR) algorithm [Kazdan and Hoppe 2013]
  We remove inaccurate vertices by assigning a quality value based on the Hausdorff distance [Cignoni et al. 1998] between points on the mesh and points on the original point cloud.
Data gaps in the point cloud
Quality map of a mesh generated with a single MK. Blue <1 mm, Green < 3 mm, Red <5 mm

## Slide 13: Data Processing and Optimization (2)
Compression - X3D Binary Format
  We reduce the file size of the model by switching to the X3D compressed binary format (X3Db) [X3DB 2015] (80% reduction => 3 MB S-reps).
  Improve initial 3D models download time
  Potential for 3D libraries of complex cases/ treatment scenarios
20th International Conference on 3D Web Technology (Web3D 2015), June 18-21, Heraklion, Crete, Greece

## Slide 14: Data Processing and Optimization (3)
Decimation vs. Accuracy – Tradeoffs
  Tested patient S-rep that was 10.568 MB in size containing 96,388 polygons
  Decimated iteratively to 80%, 60%, 40%, 20%, and 10% of the original number of polygons
Conclusion:
  5-10 scans depending on the length and width of the patient, but could still be automated, quick, and offer a maximum error as low as 10.2 mm.

## Slide 15: Results
X-Ray Therapy with Real Patient S-reps
Proton Therapy with Real Patient S-reps

## Slide 16: Acknowledgements
Co-authors
  Research Assistant, Shane Farrar, Armstrong State University, USA
  Research Assistant, Erik Leon, Armstrong State University, USA
Research collaborator
  Omar Zeidan, Ph.D., DABR, Chief, Proton Therapy Physics at UF Health Cancer Center, Orlando
Questions about the project:
  Felix.Hamza-Lup@armstrong.edu
  http://felixlup.net
  http://3drtt/org
20th International Conference on 3D Web Technology (Web3D 2015), June 18-21, Heraklion, Crete, Greece